Overview isegHAL lines and address allocation

isegConnect (especially for iCS System with a hard coded criterium inside the isegHalServer):

iseg_connect(“HV0”, “iseg-edcp://can0”, NULL);	line 0, 1, 2, 3, 4, 5 and 8, 9, 10, 11, 12
device 0 to 63
iseg_connect(“LV0”, “wiener-can://can1”, NULL);	line 0
device 0 to 63
iseg_connect(“HV1”, “iseg-scpi://usb0”, NULL);	line 6
device 0
iseg_connect(“HV2”, “wiener-scpi://usb1”, NULL);	line 6
device 1
iseg_connect(“HV3”, “iseg-scpi://com2,” NULL);	line 6
device 3

System	Alias	Interface	Connect	Lines	Device
iCS	HV0	CAN	iseg-edcp://can0	CC24 – hardware line 0 back plane / lines routed by CC24: 1,2,3,4, and 8,9,10,11 / lines 1,2,3,4 or 5 and 8,9,10,11 or 12	CC24, device 0 to 9 / CC43, device 0 to 9 / ECH238, device 0 to 63
iCS	LV0	CAN	wiener-can://can1	hardware line 0	CC24, device 0 to 9
iCS	HV1	USB	iseg-scpi://usb0	hardware line 6	CC24 or iCS mini, device 0
iCS	HV2	USB	wiener-scpi://usb1	hardware line 6	CC24 or iCS mini, device 1
iCS	HV3	RS232	iseg-scpi://com2	hardware line 6	CC24 or iCS mini, device 2
iCS	HV4	USB	wiener-scpi://usb3	hardware line 7	CC24 or iCS mini, device 0

OpcUa	can0	CAN	iseg-edcp://can0	hardware line 0	SysTec USB CANmodule 8/16
OpcUa	can1	CAN	iseg-edcp://can1	hardware line 1	SysTec USB CANmodule 8/16
OpcUa	can2	CAN	iseg-edcp://can2	hardware line 2	SysTec USB CANmodule 8/16

OpcUa	can15	CAN	iseg-edcp://can15	hardware line 15	SysTec USB CANmodule 8/16

isegConnect (especially by direct call from a client like Quasar OpcUa system):

iseg_connect(“can0”, “can0”, NULL);	line 0
iseg_connect(“can1”, “can1”, NULL);	line 1
iseg_connect(“can2”, “can2”, NULL);	line 2

iseg_connect(“can15”, “can15”, NULL);	line 15
iseg_connect(“usb16”, “iseg-scpi://usb27”, NULL);	line 16

Extended functionality of iseg_getItem and iseg_setItem by using the alias AUTO:

The call of iseg_getItem or iseg_setItem with the alias “AUTO” addresses an internal search in order to find automatically the corresponding alias form the hash. This feature is possible because the iseg_connect function registers all connected lines with the associated protocol.

The current predefinitions of the isegHAL API, iCSservice2, isegIOC, isegSnmp as well as wienerSnmp of the MPOD will be not reflected. The user have to initialize the interfaces onetime by
the connect function. The isegLibrary creates a hash with the keys HV0, HV1, HV2, LV0, LV1 and the pointers for the corresponding HAL's.
iseg_getItem(“AUTO:”, “0.1.0.VoltageMeasure”)
(SNMP: outputVoltageMeasurement.100)
(SNMP new: outputVoltageMeasurement.0100)
The internal iteration of the isegHAL hash gives following:
HV0: 0.ModuleList => 0,2,3
LV0: 0.ModuleList => 1,4 => iseg_getItem(“LV0”, “0.1.0.VoltageMeasure”) return the isegItem

iseg_getItem(“AUTO”, “6.1.2.VoltageMeasure”)
(SNMP: outputVoltageMeasurement.6102)
The internal iteration of the isegHAL hash gives following:
HV0: 0.ModuleList => 0,2,3
LV0: 0.ModuleList => 1,4
HV1: 6.ModuleList => 0
LV1: 6.ModuleList => 1 => iseg_getItem(“LV2”, “6.1.2.VoltageMeasure”)